## Slide 1: Project
Aerial Robotics (Drone)

## Slide 2: Aerial Robotics (Drone)
2024 Spring (Last Semester)
Team Competition
Goal:
  Create an algorithm to find the fastest routes to predetermined targets
  The final algorithm is implemented in a high-fidelity simulation tool
Source: ASE 497W Todd E. Humphreys; University of Texas at Austin
Notes: The first project I want to present is the Drone project I did in Aerial Robotics course last semester. This was a team competition that consisted of three people per team. The goal was to create an algorithm for the drone that would find the fastest routes to targets. The targets were balloons placed on a field, which you will see soon. And the drone had to pop the balloons by flying through them to confirm that it reached the targets. There were also imaginary obstacles that the drone had to go around,and lastly the algorithm should have worked both in a simulation environment and in real life.
So for the competition, each team would timed on how fast it pops two ballons from a designated starting point and returns to another desginated end point.
Here you see a picture of the drone, or the quadrotor that we implemented our algorithm on. Here is a picture of my proud teammates!
For spoilers, We were one of the two teams that successfully flew the dorne in real life and ended up placing 2nd in the competition.
Before I begin explaining my work, I will start by showing the result of my team’s work together!

## Slide 3: My contributions
Develop 6-DOF simulation in MATLAB
Develop A* algorithm in C++

## Slide 4: Aerial Robotics (Drone) Quadrotor Dynamics
Gravity
Force from the Fan
Disturbance
Wind Resistance
Torque from propeller acting against the air
Torque from upward thrust
Source: ASE 497W Todd E. Humphreys; University of Texas at Austin
Notes: So, before we actually worked on the algorithm to do all that, Each of us first developed a simulation that would simulate the Drone’s flight behaviors on MATLAB.
I first modeled the drone’s dynamics with 4 ODE.
The first equation was the velocity, which is just defined here.
The dynamic equation for the acceleration was determined by the forces acting on the drone. Here is the gravity acting on the drone. The second term is the upward force exerted by the fan onto the quad which keeps the drone up in the air, and we have four of those. We have the drag force acting against the motion of the quad at the end. Lastly, any disturbance force was modeled as a noise.
The third equation is for the angular acceleration. This is what you get if you take the derivative of angular velocity. Nb term is the torque combination caused by the propellers. Specifically, NB_i is the torque caused by the propeller acting against the air, so it makes the drone spin on its own axis, like this. The R cross F term is the torque caused by the thrust force that keeps the drone in air, which could make the quad flip over.
Lastly, I have the equation for the change in the attitude matrix. Notice I used the full rotation matrix to avoid singularities or gimbal lock, instead of Euler angles.

## Slide 5: Aerial Robotics (Drone) PD controller
Source: ASE 497W Todd E. Humphreys; University of Texas at Austin
Plant
Reference or desired states are denoted with a star
PD Controller
Notes: Here is the schematic of the control system I was simulating for. I used two controllers, one for trajectory control and another for an attitude control. PD controllers were implemented for both.
R star is the position of the drone, x star is the position of the x-axis of the drone’s body frame.

## Slide 6: Aerial Robotics (Drone) PD controller
Notes: But Before actually implementing PD controllers, a basic PD controller in this figure for this systmem was tuned to see how P and D gains affect the system behavior.
The goal of this exercise was to make the closed loop system’s unit step response to have less than 0.25 seconds
of rise time (Tr), less than 30 % of over shoot (Po), and less than 2 seconds of settling time (Ts) to within 2 % of reference value. .This figure shows the step response of the closed loop system with the a specific gains I chose.
Talk about how does PD affects the behavior*******************
Increasing P gain generally increases the speed of response say the reduce rise time and also reduces the setlting time.
The D gain generally decreases overshoot, but also makes it more sensitive to noise and errors.

## Slide 7: Aerial Robotics (Drone) PD controller
Attitude Controller PD Gains
Trajectory Controller PD Gains
Notes: For The actual tuning of attitude controller was really hard, because P and D gains were in matrix form for the attiude. I tuned it until the drone followed a desired circular and a designated height as closely as possible in a MATLAB simulation. Also I wanted the quad’s front to face the center of the circle throughout the flight.
In the left figure, you see the trajectory of the drone in the simulation as a blue line. It isn’t a perfect circle, but it kind of looks like a circle. The red arrows show you the direction of the quad’s “x-axis” or I can say the front of the quad. We see that mostly, it is facing towards the center of the circle. In the right figure, the goal was to get the drone to fly at 0 m, but I got as close as 0.15 m.

## Slide 8: Aerial Robotics (Drone) Sensor Modeling
GNSS Measurements
Source: ASE 497W Todd E. Humphreys; University of Texas at Austin
Source: ASE 497W Todd E. Humphreys; University of Texas at Austin
Notes: We also modeled Measurements from the GNSS antennas to find the position of the quad.
Here is the schematic of the GNSS antennas. There is one big reference antenna in the field, acting as an inertial reference frame. Although it actually is not inertial, since it is rotating with the Earth, but the inertial sensor isn’t sophisiticated enough to know that, so I was able to assume that it is inertial.
And two additional antennas are attached to the drone at its center.
So in reality and if the drone was flying and receiving GNSS measurements, the actual drone would receive according to this diagram. The position of the primary antenna in reference to the fixed antenna, rp, and also the position of the secondary antenna in reference to the primary antenna, rb
This measurement was emulated in the MATLAB simulation by taking the current actual position of the drone, adding antenna locations on the drone, and adding some noise.

## Slide 9: Aerial Robotics (Drone) Sensor Modeling
IMU
  Accelerometer Measurement Model
  Rate Gyro Measurement Model
Acceleration
Gravity
Accelerometer Noise
Accelerometer
Bias
Gyro Bias
Gyro Noise
Angular Velocity
Notes: Here is the eqeuation of model for IMU measurments. The accelerometer measurement accounts for the accleartion of itself, gravity and the bias noted as ba and noise Va.
The accleartion term is defined in the equation below, the regular asccleartion equation lot of you know, but for this, I assumed the origin of the acclearomter was fixed to the origin of the Body, which cancles out these terms.
So essentially this FB bar omega b bar equation is what defined the IMU model.

## Slide 10: Aerial Robotics (Drone)
Additional Modeling
  Camera
  Unscented Kalman Filter
Full MATLAB simulation
  Goal:
    Follow reference trajectory
      Determined by A* algorithm in C++
    Maintain 0 m altitude
Notes: Lastly, additional modleing and tool I used to complete the simulation were the camera model to detect the ballons, and the unscented Kalment filter on MATLAB that my professor provided for us for better state estimates.
With all of these models, I simulated how well the drone achieves the goal in the simulation environment, which is to follow the reference trajectory and maintain 0m altitude. In the next slide you will see the result of the MATLAB simulation I ran, and the reference trajectory I fed into it was a path determined by an algorithm that uses A* method I developed in C++, which I will explain more later.

## Slide 11: Aerial Robotics (Drone) Completed MATLAB Simulation
Notes: You see here that the drone fooloows a certain trajectory and the x-axis or the red line always points towards the direction of travel of the drone.
After seeing the controllers working well in the simulation, I now moved on to implementing a path finding algorithm on C++

## Slide 12: Aerial Robotics (Drone) C++: Path Finding Algorithm
Comparison of three different path finding algorithms in C++
  Selection Criteria:
    Number of Nodes Explored
    Number of Nodes in path
Depth First Search (DFS)
Dijkstra’s
A*
A field gridded into cells and mapped into nodes. Nodes are at the center of each cell. Red cells represent obstacles.
START
END
Notes: There were three options I considered. Depth First Serach DFS, Dijkstra’s algorithm and A* method.
How I chose one algorithm to implement was based the two criterias.
The number of nodes explored, number of nodes in path. If I explain what the picture on all the way to the right is, I think it will help understand the first criteria.
Say a field can be gridded into cells and mapped into nodes. Like the picture you see all the way to the right. The nodes exists at the vcenter of each rectangular cells. The red cells represent obstacles that the drone cannot go to.
This sort of mapping of a field is what was provided for the actual competition. The professor gave us the 3D occupancy grid that represented the actual field that the drone flew on.
So for selecting an algorithm, I used a much smaller scale and simpler 2D occupancy grid that you are seeing right here on the top right.
So back to talking about the criteria. Starting with the first criteria, So the three algorithsm have different ways of selecting which cells or nodes should be explored or not. And sometimes that algorithm could explore multiple “incorrect path” before it finds the “correct path” or other times the algorithm is smart enough to weed out certain cells right away to find the “CORRECT” path instantly without exploring other “incorrect paths”. Definitely I should prefer the latter situation, so that’s what the first criteria measures.
For the second one, it’s a much simpler criteria, that is the determined path has to be the shortest possible way, since this competition is time sensitive. For example, say if both the DFS algorithm and A* algorithm explored the same number of nodes to find its path, but obviously I would choose A* because the path it found is much shorter than the one found by DFS.
So with those criteria and also clearly seen from these pictures,
I coded all of them in C++ and tested them in the 2D test occupancy grid
The A* method was the most efficient path finding algorithm that explores the lest number of nodes and had least number of nodes in path.
Now you will see how the C++ A* algorithm I worked on looks like in the game engine simulation I was provided to work with.

## Slide 13: Aerial Robotics (Drone) Team Collaboration
Communication and Feedback
GIT
Experience at Blue helped me lead the Team to utilize GitLab
Notes: At the end, of course this competition was a team effort, and I could not have completed this project without my teammates.
The best part about having teammates is getting help from each other. When I was struggling with my part of work, my teammates had conversations with me about the relevant topics or concepts that my code pertained too. And while talking to them I would notice errors to my code. Or sometimes they would simply look at it and notice small bugs as a third person, which I didn’t notice at all by myself. We would also talk to each other give feedback to how certain codes can be better implemented, each of us would incorporate that.
I really like that and I knew the feedback would help the team, so at the beginning of this team project, I told my teammates that our team should try to communicate with each other as often as possible whether that’s text, zoom meetings or in-person meetings, so that we all will be comfortable with each other and exchange feedback and not be afraid to get or give help to each other. Our response to that was having a in-person meeting at least twice a week, we would also talk after lectures, and I really like the meetings because since we are all in the same space giving feedback was much easier than sending a text or email. And also spending time together in person also pulled the team together to work with each other even more closely.
I think it worked really well and we got a good result because of it.
I also notice the idea of active communication and feedback is one of the Blue’s leadesrship principle, “Embrace Team Blue” so I wanted to point this out.
And a short side note, I contributed to the team with my experience in GIT. I am very thankful that I struggled with GIT at Blue for a few month while I was there. None of my teammates knew how to use Git at first, so I was able to help the team set up Git repository, help if any members had issues with Git. I was glad I could do that for the team.

## Slide 14: Summary of Drone Project
Situation
A competition to pop the balloons with a drone in the least amount of time
Task
Develop MATLAB simulation
Develop path finding software for the drone
Action
Apply knowledge in dynamics, classical control theory, navigation sensors ( accelerometer, gyroscopes, GNSS receiver) for MATLAB simulation
Implemented A* method in C++ for path finding algorithm
Feedback through active Communication
Git to collaborate
Result
2nd place!
Notes: I really wanted to point this project out, because this course really felt like the software development process through SIL at Blue. Though this one is much smaller scale but it was more hands on for me since I got to develop most of the simulation and implement C++ code myself. I think these skills are super for this GNC engineering Early Career position that requires knowledge in Dyanmics, classical control theory, MATLAB, C+++ , communicatation skills, etc.
I hope this explained why this experience helps me prove I will be a good for this position.

## Slide 15
Q&A